## Slide 1
① HW MAX
• thread/warp: 32
• MAX warp/SM: 48
▶︎ Limit warp: 48
▶︎ Theoretical Occupancy: Active warp/Limit warp
SM1
block(logical unit)
warp(logical unit)
thread
③ Case2
• Suppose thread/block is 64(block size)
• Limit block/SM: 16(block limit SM)
▶︎ Limit thread/SM:
(thread/block)*(Limit block/SM)
= thread/SM= 64*16= 1024
▶︎ Active warp: 1024/32= 32
▶︎ Theoretical Occupancy: 32/48= 66.67%
② Case1
• Suppose thread/block is 32(block size)
• Limit block/SM: 16(block limit SM)
▶︎ Limit thread/SM:
(thread/block)*(Limit block/SM)
= thread/SM= 32*16= 512
▶︎ Active warp: 512/32= 16
▶︎ Theoretical Occupancy: 16/48= 33.34%
• block/SM: The block-per-SM limit is defined by the CUDA architecture itself, not by user code.
• thread/block: The number of threads per block is determined by the user when launching a kernel.
• Thread/warp: The number of threads per warp is fixed at 32 in current GPU architectures, so we don’t need to worry about it.

## Slide 2
CU
Instruction Fetch(per each WF)
WF context
WF context
WF context
WF context
SIMD
SIMD
SIMD
SIMD
Scheduler(instruction issue per each WF)
Register Files
Global
Memory Pipeline
Local Data Store
clock cycle | 1st (16-way) | 2nd (16-way) | 3rd (16-way) | 4th (16-way)
cycle 1 | R | - | - | -
cycle 2 | E | R | - | -
cycle 3 | W | E | R | -
cycle 4 | - | W | E | R
cycle 5 | - | - | W | E
cycle 6 | - | - | - | W
SIMD Unit Architecture and Parallelism
A single 16-way SIMD unit possesses 16 ALU lanes.
There are 16 parallel processing paths-one set for R (Read), E (Execute), and W (Write-it can perform individual operations on 16 different operands simultaneously.
ACE (Asynchronous Compute Engine) : work-group : CU mapping

## Slide 3
SM
Warp Schedulerx4
Scheduled Warp x4x16

## Slide 4
SM
Warp Schedulerx4
Scheduled Warp x4x16